## Slide 1: MAPA: Multi-Accelerator Pattern Allocation Policy for Multi-Tenant GPU Servers
Kiran Ranganath* Joshua D. Suetterlein Joseph B. Manzano
Shuaiwen Leon Song Daniel Wong

## Slide 2: Multi-GPU systems are increasingly common
Increased adoption of Accelerators in Top 500 Supercomputers
  GPUs
Scientific and ML applications

## Slide 3: Interconnects are becoming heterogeneous
AMD Infinity fabric
Nvidia Nvlink/NVSwitch
Compute Express Link
And more!

## Slide 4: Adopting multiple interconnects
Accelerator-based Supercomputers equipped with more than one type of interconnect technology.
Nearly 90%

## Slide 5: Accelerator topology is diverse
Nvidia DGX-1 V100
Azure NDv2
AWS P3
Facebook Big-basin
Summit

## Slide 6: Variety of communication links Variety of topologies

## Slide 7: Impact of communication links on Caffe ML training
12 GBps
25 GBps
50 GBps
(1,4)
(5,6)
(3,8)
Can lead to more than 65% slowdown.

## Slide 8: Existing allocators can cause fragmentation
 |  |  |  |  |  | 2 | 3
CPU 1
CPU 2
GPU 1
GPU 2
GPU 3
GPU 4
GPU 5
GPU 6
GPU 7
GPU 8
NVLink
QPI
PCIe
Job Queue
DGX-1 V100
Assignment based on lowest available GPU ID. Eg. Nvidia Docker
Notes: Exisiting allocators can allocate using lowest available GPU ID.

## Slide 9: Existing allocators can cause fragmentation
Assignment based on lowest available GPU ID. Eg. Nvidia Docker
 |  |  |  |  |  |  | 2
CPU 1
CPU 2
GPU 1
GPU 2
GPU 3
GPU 4
GPU 5
GPU 6
GPU 7
GPU 8
NVLink
QPI
PCIe
Job Queue
DGX-1 V100
Notes: Exisiting allocators can allocate using lowest available GPU ID.

## Slide 10: Existing allocators can cause fragmentation
CPU 1
CPU 2
GPU 1
GPU 2
GPU 3
GPU 4
GPU 5
GPU 6
GPU 7
GPU 8
NVLink
QPI
PCIe
Job Queue
DGX-1 V100
BWallocated = 12 GBps
Assignment based on lowest available GPU ID. Eg. Nvidia Docker
Notes: Exisiting allocators can allocate using lowest available GPU ID.

## Slide 11: Existing allocators can cause fragmentation
CPU 1
CPU 2
GPU 1
GPU 2
GPU 3
GPU 4
GPU 5
GPU 6
GPU 7
GPU 8
NVLink
QPI
PCIe
Job Queue
DGX-1 V100
BWallocated = 12 GBps
BWideal = 50 GBps
Assignment based on lowest available GPU ID. Eg. Nvidia Docker
Notes: Exisiting allocators can allocate using lowest available GPU ID.

## Slide 12: How often is the resource fragmentation?
Experiment
  100 randomly generated Jobs
  Each job utilizing different no. of GPUs with different execution times
  Record BWAllocated in each job
  Calculate BWAllocated / BWIdeal

## Slide 13: How to reduce fragmentation?

## Slide 14: MAPA: Multi-Accelerator Pattern Allocation
Apps
Server
App graphs
1
2
4
3
6
5
7
8
HW graph
Graph Pattern Matching (Peregrine1)
Possible Matches
1
2
3
6
7
8
4
2
3
Pattern Scoring
Allocation Policy
Allocation
Update
1
2
3
1
2
3
[1]Kasra Jamshidi, Rakesh Mahadasa, and Keval Vora. 2020. Peregrine: A Pattern- Aware Graph Mining System. In Proceedings of the Fifteenth European Con- ference on Computer Systems (Heraklion, Greece) (EuroSys ’20).
A framework to obtain nearly ideal allocations by using Graph-aware matching techniques.
1
2
3
6
7
8
4
2
3
How to score patterns?
User provided

## Slide 15: Aggregated bandwidth
Total available bandwidth in a matching pattern.
CPU 1
CPU 2
NVLink
QPI
PCIe
GPU 1
GPU 2
GPU 4
GPU 1
GPU 2
GPU 4
GPU 3
GPU 5
GPU 6
GPU 7
GPU 8
Aggregated BW
Isomorphic
App Graph
Matching pattern
50
25
25
100 GBps
Notes: Title How do I score?
Instead of

## Slide 16: Effective Bandwidth
Peak practically achievable bandwidth for any given allocation
Calculated by running NCCL All-Reduce microbenchmarks
CPU 1
CPU 2
NVLink
QPI
PCIe
GPU 1
GPU 2
GPU 4
GPU 1
GPU 2
GPU 4
GPU 3
GPU 5
GPU 6
GPU 7
GPU 8
Effective BW
Isomorphic
App Graph
Matching pattern

## Slide 17: Correlate Effective Bandwidth
VGG Training
Scoring all possible (2,3,4,5)-GPU allocations using Microbenchmarks.
Effective Bandwidth is a better metric.

## Slide 18: Benchmarking allocations at runtime is not scalable.

## Slide 19: Modeling Effective Bandwidth
Non-linear regression to predict effective bandwidth
  Number of Double NVLinks (𝑥), Single NVLinks (𝑦), and PCIe links (𝑧)
  31 samples of possible 2, 3, 4, 5 GPU combinations
Notes: Relative Error, 0.0709
Root Mean Square Error (RMSE) 1.5153
Mean Absolute Error (MAE) 7.0539

## Slide 20: Modeling Effective Bandwidth
Non-linear regression to predict effective bandwidth
Predicted Effective BW correlates well with Actual Effective BW
RMSE = 1.5153
Notes: Relative Error, 0.0709
Root Mean Square Error (RMSE) 1.5153
Mean Absolute Error (MAE) 7.0539

## Slide 21: Do we need a metric other than Effective bandwidth?

## Slide 22: Revisiting ML training speedup
Not all applications benefit from Effective Bandwidth.
BW Insensitive
Google Net

## Slide 23: How do we allocate for Bandwidth insensitive workloads?

## Slide 24: Preserved Bandwidth
CPU 1
CPU 2
NVLink
QPI
PCIe
GPU 1
GPU 2
GPU 4
GPU 1
GPU 2
GPU 4
GPU 3
GPU 5
GPU 6
GPU 7
GPU 8
Preserved BW
Preserved bandwidth is total available bandwidths with the allocation
Goal: Retain high-bandwidth links for future use
Matching pattern

## Slide 25: Allocation Policy using Effective and Preserved Bandwidths

## Slide 26: A better Allocation policy
Goal: Intelligent allocations based that suits well for the application.
BW Insensitive
BW Sensitive
Predicted Effective Bandwidth
Preserved Bandwidth

## Slide 27: Preserve Allocation policy
BW Sensitive?
App graph
HW graph
Graph Pattern Matching
Find Allocation with highest Effective BW
Find Allocation with highest Preserved BW
Yes
No
Allocation
Allocation

## Slide 28: Experimental Setup
DGX-1 : 8 V-100 GPUs
300 randomly generated jobs requiring 1-5 GPUs
Policies
  Baseline
  Topo-aware2
  Highest Aggregated Bandwidth (Greedy)
  Preserve allocation policy
[2] Marcelo Amaral, Jordà Polo, David Carrera, Seetharami Seelam, and Malgorzata Steinder. 2017. Topology-aware gpu scheduling for learning workloads in cloud environments. In Proceedings of the International Conference for High Performance Computing, Networking, Storage and Analysis.

## Slide 29: Multi-GPU optimized workloads
Neural networks (Caffe)
  VGG-16, Resnet-50, AlexNet, Inception-v3, CaffeNet, GoogleNet
Non-neural networks
  Parallel simulated annealing algorithm for global optimization (Cusimann)[1]
  Gaussian Mixture Model (GMM) [1]
  Jacobi solver[2]
[1] AngLi,ShuaiwenLeonSong,JieyangChen,XuLiu,NathanTallent,andKevin Barker. 2018. Tartan: Evaluating Modern GPU Interconnect via a Multi-GPU Benchmark Suite. In 2018 IEEE International Symposium on Workload Characteri- zation(IISWC).
[2] GTC 2019. Multi-GPU Programming Models. https://developer.download. nvidia.com/video/gputechconf/gtc/2019/presentation/s9139- multi- gpu- programming- models.pdf

## Slide 30: 50% of jobs with MAPA have better bandwidth allocation than all jobs in Baseline/Topo-aware
Higher the better→
Notes: Cusimann - annealing algorithm for global optimization
Gaussian Mixture Model (GMM)
Jacobi solver
BW Sensitive is a different

## Slide 31: Preserve policy does not starve insensitive workloads
Higher the better→
Notes: Cusimann – CUDA simulated annealing algorithm for global optimization
Gaussian Mixture Model (GMM)
Jacobi solver
We did not worsen the bandwidth for insensitive
BW Sensitive is a different

## Slide 32: Reduced execution time with better allocations
Lower the better←

## Slide 33: No performance degradation among BW-insensitive workloads

## Slide 34: System throughput improvement over baseline
Nearly 12% improvement with Preserve.
Notes: Axis labels

## Slide 35: Exploring future topologies

## Slide 36: How will MAPA perform on future hardware topologies?
Simulate 16-GPU hardware topologies
Regular
Irregular

## Slide 37: Improved Effective bandwidth in 16-GPU Torus-2d
Greedy performed better for 75% due to less irregularity in hardware topology

## Slide 38: Improved Effective BW in 16-GPU Cube-mesh
Preserve performed better for 25%, 50%, and 75% due to more irregularity in hardware topology

## Slide 39: Conclusion
Communication Links and topologies in multi-accelerator systems
  Increasingly becoming heterogeneous and complex
  Presents challenges in allocations (fragmentation)
Multi-Accelerator Pattern Allocation (MAPA) System
  Graph Pattern Matching approach
  Preserve allocation policy
    Pattern scoring metrics – Effective and Preserved Bandwidth
  12% system throughput improvement over baseline
  35% improved worst-case execution time over baseline
https://github.com/socal-ucr/mapa

## Slide 40
Thank you!
Q & A

## Slide 41: Better AggBW may not improve performance
VGG Training
Why?

## Slide 42: Overhead of pattern lookup
Overhead is in the order of hundreds of milliseconds
We observe moderate overheads when
  Application graphs have 9 or more edges and,
  Hardware graphs have 120+ edges
The statistics are upper-bound
Future optimization: Parallel scoring

## Slide 43: Extracting Application topologies
Source Code Analysis
  Identifying CUDA and NCCL APIs
Runtime Analysis
  Number of Nvlink packets

## Slide 44: Determine BW sensitivity
More calls should have >105 bytes
Enough number of calls to amortize

## Slide 45: Greedy Allocation policy
App graph
HW graph
Graph Pattern Matching
Find Alloc with highest Aggregated BW
Allocation

## Slide 46: Predicted Effective Bandwidth
Running microbenchmarks not scalable
Non-linear regression to model effective bandwidth
  31 samples of possible 2, 3, 4, 5 GPU combinations
Linear
Inverse linear
Pairwise
Inerse pairwise
triplet
Inverse triplet
Calculated Weights

## Slide 47: Simulate future topologies and policies
Hardware Topologies
  More accelerators
Application Topologies
  Different communication patterns
Allocation Policies
  Pattern scoring
Job File
ID, NumGPUs, Topology, BW Sensitive 1, 3, Ring, True 2, 4, Tree, False ….
Hardware graph
Log File
ID, Allocation, Topology, Effective BW (GBps) 1, (1,2,3), Ring, 45 2, (5,6,7,8), Ring, 48 ….
MAPA Simulation framework

## Slide 48: Simulation Framework
Job File
ID, NumGPUs, Topology, BW Sensitive 1, 3, Ring, True 2, 4, Ring, True 3, 5, Tree, False 4, 4, AllToAll, True ….
Dispatcher
 |  |  |  | 6 | 5 | 4 | 3
MAPA
Hardware graph
Allocation
1
2
4
3
6
5
7
8
Simulation Execution Engine
1 | 2 | 6 | 5
4 | 3 | 7 | 8
Job ID: 1
Job ID: 1
Job ID: 1
Job ID: 2
Job ID: 2
Job ID: 2
Job ID: 2
Log File
ID, Allocation, Topology, Effective BW (GBps) 1, (1,2,3), Ring, 45 2, (5,6,7,8), Ring, 48 ….
Job Finished
Job Finished
Job Start
Job ID: None
Deallocate
Job Queue
App Graph
Update (Allocate/ Deallocate)
Retrieve Available HW graph
Allocate
A mechanism to explore novel
  Hardware Topologies
    Cost-effective
    Point-to-point
  Application Topologies
  Allocation Policies

## Slide 49: Evaluating MAPA Simulation framework
EffectiveBW obtained during real and simulations correlate